## Slide 1
After improvement
Breakthrough
Before improvement
Model filter buttons on the Lot screen module list
Install PCB - model selection at changeover (Lot screen)
PHENOMENON
IMPROVEMENTS
At every changeover the operator had to scroll through a flat list of 113+ modules, in load order, to find the model to run.
EFFECT:
Finding the model at changeover now takes one tap plus a short list.
DX Level 구분 |  | 
A2D | 정보화 | 지능화
개선 영역 | Analog BP | DX BP
이물/생산성 |  | 
성능/품질 | ○ | 
프로세스 |  | 
안전환경 |  | 
고객가치 |  | 
전파 | 광학 | 기판 | 전장 | CTO | 전자 | 생기 | 품질
 | ○ | △ | △ | △ | △ | X | X
PROBLEM
Model filter buttons added above the module list. Each button is a model number (1-15) and shows the variants it has (L, R, X). One tap shows only that model; TODOS shows the full list.
No grouping by model: variants of the same model (L, R, X and revisions MM00, MM10, MM20...) were scattered across the list.
The search was slow and it was easy to pick a similar name by mistake, on a step that is on the critical path of the changeover.
■ Date : 18/09/2026 ■ Writer : Guillermo Carrillo ■ Division: CM ■ Team: Production
IMPACT:
About 35 s saved per changeover in the model search.
Lower risk of picking the wrong model: only its variants are shown.
Applicable to other stations with the same Lot screen.
TODOS keeps the full list available and CHANGE works as before, so the operator workflow stays the same.
Before: one flat list, load order (113+ entries)
After: filter by model number (model 6 selected → 10 entries)
How the module name maps to the buttons
ACS05S
family
006
model → button
L
L / R / X
.MM00
revision
~45 s
search before
~10 s
search after
-78%
search time
113+
entries to scan before
~10
entries per model
Line 2 with all updates
20,127 pcs on 2 Oct vs 16,678 on 12 Aug (+20.7%). 1 Oct: 17,449 pcs (controlled material), best hour 1,003.
Search times are approximate operator observations; effect on total changeover time still to be measured. Line data: hourly production report, TOP TLA Line 1.